## Slide 1: Fundamental limits to electromagnetic response by convexity, causality, and duality
Owen Miller
Yale Applied Physics & Energy Sciences Institute
Andrew Shim, Qingqing Zhao, Haejun Chung
“Fundamental Limits to Near-Field Optical Response over Any Bandwidth”
“Maximal Free-Space Concentration of Light”
“Minimum Mode Volume of Dielectric Resonators”
millergroup.yale.edu/talks
millergroup.yale.edu/publications

## Slide 2: Design & Optimization with Waves Owen Miller, Yale Applied Physics
The design challenge:
Lots of degrees of freedom in geometry,
but what structure is best for given device & materials?
And what performance & phenomena are possible?
Bottom-up Large-scale optimization
Top-down Optical-response bounds
Rapidly discover superior, non-intuitive structures
Identify fundamental limits,
subject only to Maxwell’s equations
Theory + Computation + Expt. collaborators

## Slide 3: Recent Results
Optimal nanoparticle forces, torques, and illumination fields
ACS Photonics 6, 395 (2019)
High-NA Achromatic Metalenses by Inverse Design
High-steering-angle metasurfaces by inverse design
Brightness Theorems for Waves
Optica 6, 1321 (2019)
Submitted, arXiv: TBD (2019)
arXiv: 1905.09213 (2019)

## Slide 4: Today
Power-bandwidth limits to optical response
  convexity (passivity) + analyticity (causality) for maximum response
Maximum free-space concentration of light
  Going beyond the diffraction “limit”: tradeoffs and bounds via convex relaxations of quadratic programs
Computational bounds, via duality
  Multi-frequency and/or fabrication tolerance constraints

## Slide 5
The scattering problem at frequency
scatterer(s)
Passive convolution operators (Herglotz functions):
material susceptibility:
Green’s function:
“Near-field:” point sources, close () to a scatterer
Notes: Note that chi and G are generally 6x6 tensor fields

## Slide 6
Near-field nanophotonics
Prototypical quantity: spontaneous emission
Related response functions:
CDOS
RHT
Casimir
Smith-Purcell
Raman
Fundamental question: How large can these effects be, over any bandwidth, for any material & patterning?

## Slide 7: Bounds to Light–Matter Interactions
For any lossy material (), we can use energy conservation to derive general, shape-independent upper bounds at a single frequency
  absorption/scattering
  local density of states
  radiative heat transfer
  high-radiative-efficiency plasmonics
  2D materials, nonlocal materials
  Smith-Purcell radiation / Cherenkov / EELS
For any material, using energy conservation + causality, we can derive upper bounds over any nonzero bandwidth of interest
Predict a “material FOM:” dielectric vs. metal, 2D/3D, etc.
Opt. Exp. (2016)
PRL (2015)
Nano Lett. (2017a)
Nano Lett. (2017b)
Nat. Phys. (2018)
PRX (2019)

## Slide 8: Bounds to Light–Matter Interactions
For any lossy material (), we can use energy conservation to derive general, shape-independent upper bounds at a single frequency
  absorption/scattering
  local density of states
  radiative heat transfer
  high-radiative-efficiency plasmonics
  2D materials, nonlocal materials
  Smith-Purcell radiation / Cherenkov / EELS
For any material, using energy conservation + causality, we can derive upper bounds over any nonzero bandwidth of interest
Predict a “material FOM:” dielectric vs. metal, 2D/3D, etc.
Opt. Exp. (2016)
PRL (2015)
Nano Lett. (2017a)
Nano Lett. (2017b)
Nat. Phys. (2018)
arXiv (2018)

## Slide 9
Local density of states, LDOS
LDOS ~ power radiated by (electric) dipole
Work done by current J on field E:
= total power radiated
Work done by field E on current J:
= emitter location
= emitter polarization
= Green’s function

## Slide 10: General limits to optical response
Total spontaneous emission ~ Im(scattering amplitude)
[Owen Miller et. al, Opt. Exp. 24, 3329 (2016)]
total SE ~ total LDOS ~ linear in response
nonradiative LDOS = dissipation ~ quadratic
total SE (rad. + nonrad.) > nonrad. SE
induced current
power
unphysical

## Slide 11: General limits to optical response
[Owen Miller et. al, Opt. Exp. 24, 3329 (2016)]
At a single (real) frequency:
material enhancement
near-field enhancement
Notes: depends on dimensionality, local vs nonlocal, etc.

## Slide 12: The upper bounds are tight
[Owen Miller et. al, Opt. Exp. 24, 3329 (2016)]
…at least at the surface-plasmon frequency of a metal
LDOS, computed
LDOS limit
Notes: depends on dimensionality, local vs nonlocal, etc.

## Slide 13: All-frequency bounds: LDOS sum rule
causal linear response function
Notes: depends on dimensionality, local vs nonlocal, etc.

## Slide 14: Power–bandwidth limits
Optical theorems: special quantities (e.g. extinction, LDOS) can be written as , where
is linear in the total field, leading to convex constraints and single-frequency bounds
is a causal linear-response function, analytic in the UHP (leading to all-freq sum rules)
Items #2 and #3 share the same origin!
We can use this connection for bounds over any bandwidth
Notes: These two ideas had developed in parallel, seemingly unrelated

## Slide 15
Freq-averaged LDOS
How to compute average response over bandwidth ?
Simplest approach:
More generally:
window function

## Slide 16
Freq-averaged LDOS = complex-freq LDOS!
analytic in the upper-half of the complex-⍵ plane
poles determined by function, ,
Simplifies bandwidth-averaged problem to a single (complex) frequency. Still: how large can be?

## Slide 17: Upper bounds to bandwidth-avg LDOS
Physical Review X 9, 011043 (2019)
At a single (real) frequency:
Averaged over bandwidth around center freq
and is a “material figure of merit”
where
Notes: depends on dimensionality, local vs nonlocal, etc.

## Slide 18
Material performance vs center wavelength
Notes: Now we compare the material fom for metal and dielectrics, whose fom simplifies. As wavelength increases, metals have larger and larger negative real part of permittivity, and so fom increases with wavelength. For dielectrics, since permittivity remains constant with wavelength, their fom does so as well.
-the results themselves are not surprising, we know that silver is better than gold at visible and infrared frequencies.
-but it is really worth pointing out the fact that we can quantitatively predict which materials are superior to others
-here we fixed the bandwidth ratio to be 0.1, but we can also see how these materials perform with changing bandwidth…

## Slide 19
Material performance vs bandwidth
Notes: The behavior here can be understood from the fact that imaginary frequency is equivalent to adding loss to the system. Metals are already lossy, and so a small enough delw doesn’t affect its behavior, whereas dielectrics are lossless and so are very sensitive to even a small loss from imaginary frequency.

## Slide 20
Δω/ω0 = 0.1
2D vs 3D material
ρ 1/d4
ρ 1/d3
Notes: We can also compare bulk materials to 2d materials. Here we show bound on average ldos that scales as 1/d^4 for 2d and 1/d^3 for 3d, arising from our framework. The dividing line depends on the material properties (here we chose drude-like materials), but we can conclude from our framework that in general 2d materials have a bigger potential than 3d for smaller separations.

## Slide 21: Today
Power-bandwidth limits to optical response
  convexity (passivity) + analyticity (causality) for maximum response
Maximum free-space concentration of light
  Going beyond the diffraction “limit”: tradeoffs and bounds via convex relaxations of quadratic programs
Computational bounds, via duality
  Multi-frequency and/or fabrication tolerance constraints

## Slide 22: Superresolution: spot sizes << λ
Optical resolution: a foundational imaging metric
Superresolution: resolution below diffraction limit
Approaches to superresolution:
a priori information (Betzig, Hell, Moerner, et al.)
near-field scatterers/probes (Fink, Ammari, et al.)
quantum metrology (Tsang, Lu, et al.)
far-field beam interference (“superoscillations”) M. Berry, Aharonov, Zheludev, Eleftheriades, Rogers, et al.

## Slide 23: Superoscillations: “Faster than Fourier”
Fourier analysis: oscillations of a signal not strictly limited by maximum Fourier component (Slepian 1961, Levi 1965, Ferreira 2006, etc.)
Chen, Wen, & Qiu, Light: Science and Applications (June 2019)

## Slide 24: Superoscillations: “Faster than Fourier”
Fourier analysis: oscillations of a signal not strictly limited by maximum Fourier component (Slepian 1961, Levi 1965, Ferreira 2006, etc.)
Best-known computational bounds (Sales & Morris 1997) require a scalar-wave approximation of weakly scattering rotationally symmetric apertures
Recent advances in metasurface have led to significant efforts at design and experiment
Huang, CW Qiu et al. Laser Photonics Rev 8, 152 (2014)
Qin, Hong et al. Sci. Rep. 5, 9977 (2015)
N. Zheludev Nature Materials 7, 420 (2008)
F. Huang et al. J. Opt. A 9, S285 (2007)
see also: Dholakia, Berry, Eleftheriades, Noda

## Slide 25: The superresolution problem
for any excitation…
maximize the field intensity at the origin, given a desired spot size
field
maximize
subject to

## Slide 26: Superresolution: our approach
(surface) equivalence principle  encapsulate the beam-generation structures with surface currents in free space

## Slide 27
Now the problem is
maximize
subject to
No prescription for analytical bounds
: GF from equivalent currents to origin
where
: GF from equivalent currents to zero-field contour

## Slide 28
Now the problem is
maximize
subject to
No prescription for analytical bounds.
Transformations, towards global analytical bounds:
project onto currents that satisfy zero-field constraint
do separate maximization over polarization at origin
Fourier decomposition at origin, keep N lowest-order modes

## Slide 29
Follow the algebra and…
general upper bounds!
For any aperture, beam-generation mechanism, focal spot, etc., the maximum intensity at the origin is
For the typical case of a planar aperture and far-zone beam, the Strehl ratio (max intensity / Airy max) is:
η is a normalized spot-size radius,

## Slide 30
reciprocity-based intuition
Smax, bound
Airy beam
Strehl Ratio, S (Focal Intensity / Airy)
how does the current state-of-the-art (SOA) compare?
Are better designs possible?

## Slide 31: “Inverse Design” (adjoint-based optimization): A classical control technique, newly emerging in photonics
A. Jameson JSC 3, 233 (1988)
O. Pironneau JFM 64, 97 (1974)
Bendsoe & Sigmund,
“Topology Optimization” (2003)
Aerodynamics
Elasticity
Altair PDG
Boeing
Photonics
Miller, Ganapati, Keraly et al. (2012-)
Vuckovic et al. Nat. Phot. 9, 374 (2015)
Fast computation of derivatives, for any !
Deep Learning
Rumelhart et al. Nature 323, 533 (1986)
Werbos, “The Roots of Backpropagation” (1994)
Sigmund, Rodriguez, Engheta, SGJ, S/J Fan, etc.
Notes: This method goes back to studies of designs in fluid flow, aerodynamics, and elasticity

## Slide 32
Inverse design of super-resolving metasurfaces approaching fundamental limits
(b)
(c)
(d)

## Slide 33: Superresolution: alternative formulations
max.
s.t.
or
or
FWHM constraint
Local wavevector
for latter two, bounds can be found via semidefinite relaxations:
zero-field constraint
Zero-field spot size
Strehl ratio, S
Strehl ratio, S
Strehl ratio, S
FWHM spot size
Local wavevector

## Slide 34: Superresolution: alternative formulations
max.
s.t.
or
or
FWHM constraint
Local wavevector
for latter two, bounds can be found via semidefinite relaxations:
zero-field constraint
Zero-field spot size
Strehl ratio, S
Strehl ratio, S
Strehl ratio, S
FWHM spot size
Local wavevector

## Slide 35: Superresolution: alternative formulations
max.
s.t.
or
or
FWHM constraint
Local wavevector
for latter two, bounds can be found via semidefinite relaxations:
zero-field constraint
Zero-field spot size
Strehl ratio, S
Strehl ratio, S
Strehl ratio, S
FWHM spot size
Local wavevector

## Slide 36: The mode-volume problem
“Mode volume” is a measure of the spatial concentration of an electromagnetic mode
For a number of applications, one wants the smallest mode volume possible (apps: spontaneous-emission enhancements, nonlinear freq generation, nanolasers, etc…)
There has been significant design effort:
(high-Q)

## Slide 37: What is the smallest possible mode volume? Without constraints, it is zero, 0. The fields near a sharp tip diverge,  zero mode volume In reality, fabrication constraints prevent perfectly sharp tips. How to find bounds subject to such constraints?
Andersen and Solodukhov, IEEE TAP AP-26, 598 (1978)

## Slide 38: Computational bounds via duality
Typical: replace (nonconvex) Maxwell equation constraint with simpler (typically convex) constraint. Can we keep Maxwell?
For mode volume, the problem is:
defines on a grid of given fabrication resolution
Try to directly find Lagrangian dual with Maxwell constraint
Inspiration: “Computational Bounds for Photonic Design,” Angeris/Vuckovic/Boyd, ACS Photonics 6, 1232 (2019)

## Slide 39: Dual formulation of mode-volume min.
We “lift” the quadratic constraint to a linear one
The dual is a convex QCQP
Dual problem can be solved by Gurobi or other standard optimization toolboxes

## Slide 40: Mode-volume: guess optimal structures

## Slide 41: Mode-volume bounds

## Slide 42: Dual-frequency mode-volume bounds
A really nice perk of the duality approach is that we can seamlessly accommodate two-frequency (and multi-frequency) designs, as required e.g. in nonlinear optics

## Slide 43: Looking forward
Large-scale comp. optimization
General bounds for light–matter interactions
Near field offers tremendous opportunity:
  100–1000X enhancements in LDOS
Maximum-efficiency superresolving beams can be defined, and achieved with metasurfaces
Lagrangian duality: an approach for Maxwell-constrained bounds

## Slide 44: Supplementary Materials

## Slide 45: Radiative Heat Transfer
Stefan-Boltzmann
Kirchoff’s Law:
absorptivity = emissivity
= 1
image:Wikipedia
Far-field
Near field
Difficulty: comp/expt
progress is very recent
e.g. for future
thermo-photovoltaic systems?
hot
PV cell
heat
photons
In the near field, (evanescent) thermal transport can exceed “black-body” limit
Wang et. al. Nat Nano 9, 126 (2014)
“blackbody” definition (ray-optical)

## Slide 46: Upper limits to near-field heat transfer
Heat flux between a hot body of temp. T and a cold body is bounded above by:
material enhancement factors
for a minimum separation d between extended objects:
near-field enhancement
~ 1/d2
Lorentzian-weighted average of electric/magnetic LDOS
Stefan-Boltzmann

## Slide 47
Limits on what is possible: Examples
Shockley–Queisser limit to solar-cell energy-conversion efficiency
Black-body limit on thermal radiation (ray optics, in far field for linear and/or equilibrium surface)
Wheeler–Chu bounds on antenna quality factor Q (per V)
Shannon bounds on channel information capacity
…
Frequency,
Scattering quantity,

## Slide 48
Linear wave scattering
incident light,
wavelength λ,
intensity I0
scatterer
scattered light, power Pscat
How much power can the body scatter/absorb/radiate/etc.?
…for a given volume of material (or emitter–scatterer separation),
...and a given frequency or bandwidth
local, linear materials: 6x6 susceptibility χ(x,)
frequency domain, passive materials:
(i.e., polarization currents cannot supply energy)
(scatterer = nanoparticle / metasurface / waveguide / etc.)

## Slide 49: Optical theorem: Power ~ Im[amplitude]
Extinguished power (absorption + scattering) is proportional to the (imaginary part of) the overlap of the incident field and the induced polarization currents
linear in
extinction (abs. + scat.) > absorption
induced current
power
unphysical
absorption is quadratic in
meanwhile…

## Slide 50: the rest is easy: Optimize desired objective subject to absorption ≤ extinction (typically a convex optimization problem, can be solved analytically)

## Slide 51: General limits to optical response
By energy conservation, variational calculus and standard optimization theory (optimality conditions)…
[Owen Miller et. al, Opt. Exp. 24, 3329 (2016)]
(∂Pabs/∂Pind = 0, etc.)
absorption
scattering
Ideal materials for smoke grenades

## Slide 52: Bounds to Light–Matter Interactions
For any lossy material (), we can use energy conservation to derive general, shape-independent upper bounds at a single frequency
  absorption/scattering
  local density of states
  radiative heat transfer
  high-radiative-efficiency plasmonics
  2D materials, nonlocal materials
  Smith-Purcell radiation / Cherenkov / EELS
For any material, using energy conservation + causality, we can derive upper bounds over any nonzero bandwidth of interest
Predict a “material FOM:” dielectric vs. metal, 2D/3D, etc.
Opt. Exp. (2016)
PRL (2015)
Nano Lett. (2017a)
Nano Lett. (2017b)
Nat. Phys. (2018)
PRX (2019)

## Slide 53: Low-loss plasmonics

## Slide 54: Hybrid dielectric–metal resonators
Metal film: provides subwavelength (~quasistatic) resonance
Dielectric nanoparticle: lateral confinement and large
with Yi Yang
(MIT)
Previous hybrid approaches:
Maksymov,
Lalanne et al. PRL 105, 180502 (2010)
Outlon, Zhang et al. Nat. Phot. 2, 496 (2008)

## Slide 55: Near-field enhancements w/ dielectric-on-metal
Near-field spontaneous emission enhancement: Simultaneous large enhancement (>5k) and high radiative efficiency (90%, >75% photon)
Previous all-metal approaches (theory):
5k & <30%
4k & ≈20%
Yang et al. Nano Lett. 16, 4110 (2016)
Mikkelson et al., Nat. Phot. 8, 836 (2014)
10k & 20%
Faggiani et al., ACS Phot. 2, 1739 (2015)
Yang, Miller et al. Nano Letters 16, 4110 (2017)

## Slide 56: Free-electron radiation
Three pathways for free, charged particles to radiate, at constant velocity:
Cherenkov radiation (within medium)
Smith–Purcell radiation (near medium)
Transition radiation (across material boundary)
Fundamental question:
How much spontaneous radiation can be extracted from free electrons?
(EELS)
Notes: Note that Smith-Purcell formula connect radiation wavelength to the electron speed, structure period, angle, etc. But at what intensity?
Need to have applications at finger tip

## Slide 57
Surprising prediction: slow electrons can be optimal
separation,
velocity,
Bound on radiation / EELS, via earlier prescription:

## Slide 58: Experimental probe of theoretical bound
Yang et al., Nat. Phys. 14, 894 (2018)

## Slide 59: Outline
Large-scale computational design: subwavelength absorbers for solar cells
Bounds to general EM scattering response
  linear wave scattering in absorptive systems
  graphene, 2D materials
  hydrodynamic nonlocality
  low-loss plasmonics
Free-electron radiation
Near-field radiative heat transfer

## Slide 60: Geometry-dependent cross-section bounds
incident planewave
in vacuum
scattered power
χ
scatterer
(E dipole)
(E quadrupole)
(N multipoles)
…
Spherical scatterers: Hamam et al. PRA 75, 053801 (2007)
Generic scatterers: Yaghjian JAP 80, 2547 (1996)
Ruan & Fan APL 98, 43101 (2011)
Liberal et al. IEEE TAP 62, 4726 (2014)
Scattered-field operator: Hugonin, Besbes, and Ben-Abdallah PRB 91, 180202 (2015)
… depends non-trivially on shape
(N ~ diameter as size ⟶ ∞)
but not on the materials!
Kwon & Pozar IEEE TAP 57, 3720 (2009)

## Slide 61: How tight are these bounds?
plane-wave excitation:
the limits are “tight” across many frequencies
for absorption and scattering

## Slide 62: “Best” materials vs. wavelength
dashed lines: optimal ellipsoids require aspect ratios > 30:1

## Slide 63: Low-loss plasmonics

## Slide 64: Hybrid dielectric–metal resonators
Metal film: provides subwavelength (~quasistatic) resonance
Dielectric nanoparticle: lateral confinement and large
with Yi Yang
(MIT)
Previous hybrid approaches:
Maksymov,
Lalanne et al. PRL 105, 180502 (2010)
Outlon, Zhang et al. Nat. Phot. 2, 496 (2008)

## Slide 65: Near-field enhancements w/ dielectric-on-metal
Near-field spontaneous emission enhancement: Simultaneous large enhancement (>5k) and high radiative efficiency (90%, >75% photon)
Previous all-metal approaches (theory):
5k & <30%
4k & ≈20%
Yang et al. Nano Lett. 16, 4110 (2016)
Mikkelson et al., Nat. Phot. 8, 836 (2014)
10k & 20%
Faggiani et al., ACS Phot. 2, 1739 (2015)
Yang, Miller et al. Nano Letters 16, 4110 (2017)

## Slide 66: Bound response from 2D Materials? polarization currents  surface currents susceptibility  conductivity

## Slide 67: 2D Materials: Bounds & material FOM
O. D. Miller et. al, Limits to the Optical Response of Graphene & 2D Materials, Nano Letters (Aug. 2017)
Bounds on cross-section:
…and for near-field quantities:
(LDOS)
(NF RHT)

## Slide 68: How tight are these bounds?
plane-wave excitations:
the limits are “tight” (or nearly so) across many frequencies
ellipses
“pinched” ellipses

## Slide 69: “Best” materials vs. wavelength

## Slide 70: Towards quantum: hydrodynamic nonlocality
At <10nm sizes & length scales, bulk no longer valid
In 2–10nm range, for certain materials, can approximate susceptibility/conductivity with a hydrodynamic model:
“convection”
“diffusion”
Mortensen et al. Nat. Comm. 5, 3809 (2014)
DR Smith et al. Science 337, 1072 (2012)

## Slide 71: Convex constraint for nonlocal response
Write absorbed power in terms of currents:
Similarly, extinction:
quadratic in and
linear in and
Hydrodynamic current–field relationship:

## Slide 72: Tighter bounds for nonlocal response
Consider a figure of merit = extinction / local density of states:
Far-field extinction
Define
= scatterer size
= “diffusion length”
Near-field LDOS
Nano Letters 17, 5408–5415 (Aug. 2017)
Notes: Interesting note: bounds only depend on D, resistive component, not beta, reactive component

## Slide 73: Common FOM: High Radiative Efficiency
Often want to optimize response such that radiative efficiency () >
Nat. Mat. 9, 205 (2010)
solar cells, LEDs, …
Example:

## Slide 74: Maximum free-electron radiation
Field emanating from an electron at speed :
Bound on radiation / EELS, via earlier prescription:
: impact parameter

## Slide 75: Large scattering efficiencies

## Slide 76: Takeaways
For a surprising variety of nanophotonics phenomena, we can derive upper bounds to what is possible
There is a simple material figure of merit that universally dictates maximal response
There appears to be tremendous opportunity for improvement in the near field, through patterning/structure
(3D)
(2D)
Approaches that won’t work:
Hyperbolic metamaterials
Emergent effective-medium
Epsilon-near-zero
Hydrodynamic nonlocality
…
Notes: %$Note that in TPV conductive heat is waste.