## Slide 1
How insects fly:
the attached leading-edge vortex and
its vorticity dynamics
2023 IASM-BIRS WORKSHOPS
Dr. Long Chen
Assistant Professor
Beihang University, China
Notes: 各位专家好。首先向大家表示歉意，因为周末需要到上海出差，所以无法线下参加答辩。我是来自北航交通学院的陈隆，现工作岗位为助理教授。

## Slide 2
List of contents
1
Aerodynamics of Flying Insects
Leading-edge Vortex Stability
Vorticity Dynamics of LEV
2
3
Notes: 我将从以下三个方面向各位汇报工作

## Slide 3
List of contents
1
Aerodynamics of Flying Insects
Leading-edge Vortex Stability
Vorticity Dynamics of LEV
2
3
Notes: 我将从以下三个方面向各位汇报工作

## Slide 4
Aerodynamics of Flying Insects
Insects and birds are excellent flyers in nature!
Bee
Moth
Hummingbird
Mosquito
Dragonfly
Horizontal flapping
Vertical flapping
Wright Brothers 1910s
Airplanes & Helicopters in 2020s
Inspiration
Micro air vehicles
Scale down
E.P. Frost's 1902
×
√

## Slide 5
Aerodynamics of Flying Insects
Bio-inspired micro air vehicles become popular and focus
Reconnaissance
Swarm
Rescue
Soldier weapon
2018
2019
2019
2022
2015
2020
Dragonfly
Butterfly
Delfly I
Robobee I
Robobee II
Delfly II
Toy

## Slide 6
Aerodynamics of Flying Insects
Steady aerodynamics fails to explain an insect flight
An insect-like flapping wing at a high angle of attack can not generate sufficient lift for flight!
Obviously not true!
Leading-edge
vortex
Absence of stall as a critical mechanism!
Absence of Stall & Dynamic Stall

## Slide 7
Aerodynamics of Flying Insects
The formation of stable LEV is a common feature of insects
Liu, H. & Aono, H. (2009). Size effects on insect hovering aerodynamics: an integrated computational study.
How does the flapping/revolving motion stabilize the LEV?

## Slide 8
List of contents
1
Aerodynamics of Flying Insects
Leading-edge Vortex Stability
Vorticity Dynamics of LEV
2
3
Notes: 我将从以下三个方面向各位汇报工作

## Slide 9
Leading-edge Vortex Stability
Hypotheses to explain a stable LEV on flapping wings
D. Lentink & M. H. Dickinson. (2009). Rotational accelerations stabilize leading edge vortices on revolving fly wings.
Spanwise convection:
driven by spanwise (tipward) flow
Pressure gradient motivates the tipward flow
Re-dependent (strong at Re>1000)
Not well defined (velocity, helicity, etc.)
Rotational accelerations:
centrifugal and Coriolis accelerations
(maybe) Related to spanwise convection
AR-dependent (strong at AR<3)
Not well explained (dynamic forces vs. vorticity)

## Slide 10
Leading-edge Vortex Stability
Hypotheses to explain a stable LEV on flapping wings
C. J. Wojcik & J. H. L. Buchholz. (2014). Vorticity transport in the leading-edge vortex on a rotating blade.
J. M. Birch & M. H. Dickinson. (2001). Spanwise flow and the attachment of the leading-edge vortex on insect wings.
Downwash:
reduction of effective angle of attack
Re=110
Limited parameter space
Vorticity annihilation:
interaction between the LEV and the opposite-sign layer
Re=4000
A minor contribution

## Slide 11
Leading-edge Vortex Stability
Hypotheses to explain a stable LEV on flapping wings
The LEV stability is relevant to Reynolds number, aspect ratio (span over chord) and Rossby number (or root cutoff).
The local LEV stability at a specific spanwise position may be relevant to revolving radius.
The LEV dynamics is time-variant and dependent on revolving radius during the LEV formation.
The LEV dynamics is still underexplored and requires a temporo-spatial analysis under a universal approach.

## Slide 12
List of contents
1
Aerodynamics of Flying Insects
Leading-edge Vortex Stability
Vorticity Dynamics of LEV
2
3
Notes: 我将从以下三个方面向各位汇报工作

## Slide 13
Vorticity Dynamics of Leading-edge Vortex
Problem setup and frames
Inertial Cartesian frame → rotating Cartesian frames
Due to the revolving nature
Related to azimuth angle () and fixed during the motion
For a specific point A:
  Positive radial direction
  (from point A to the center of rotation)
  Positive tangential direction
  (tangential and backward to the wing motion)
  Vertical direction is preserved
Gradient tensors are calculated using chain rules

## Slide 14
Vorticity Dynamics of Leading-edge Vortex
Vorticity equation in the co-rotating frame
Navier-Stokes equations
Normalized vorticity transport equation (co-rotating frame)
Radial components (r-direction)
Tilting
Stretching

## Slide 15
Vorticity Dynamics of Leading-edge Vortex
Simulations and PTV experiments
Numerical simulations
Robotic wing experiments
An in-house solver
  Artificial compressibility method
  Body-fitted O-H block
  Well validated
Oil tank with ‘Shake-the-box’ PTV setups
  Dynamically-scaled
  Time-resolved 3D flow measurement
  Force measurement (Nano17)
L. Chen, J. H. Wu and B. Cheng. (2020). Leading-edge vortex formation and transient lift generation on a revolving wing at low Reynolds number.

## Slide 16
Vorticity Dynamics of Leading-edge Vortex
Benchmark（ Re=1500 AR=3 Ro=2.56）
CFD
PTV
^
A conical LEV
Stable LEV region
Unstable LEV region
Intensity saturation

## Slide 17
Vorticity Dynamics of Leading-edge Vortex
Benchmark（ Re=1500 AR=3 Ro=2.56）
Tangential convection of radial vorticity represents the spreading of LEV into the downstream
Vertical convection of radial vorticity represents the downwash effect in LEV stability
^

## Slide 18
Vorticity Dynamics of Leading-edge Vortex
Benchmark（ Re=1500 AR=3 Ro=2.56）
^
Radial convection of radial vorticity represents spanwise convection effect in LEV stability
Spanwise convection is limited within the stable LEV region

## Slide 19
Vorticity Dynamics of Leading-edge Vortex
Benchmark（ Re=1500 AR=3 Ro=2.56）
^

## Slide 20
Vorticity Dynamics of Leading-edge Vortex
Benchmark（ Re=1500 AR=3 Ro=2.56）
^
Planetary vorticity tilting (PVT)
Coriolis acceleration
PVTr is the vertical gradient of tangential Coriolis acceleration
PVTt is the vertical gradient of radial Coriolis acceleration

## Slide 21
Vorticity Dynamics of Leading-edge Vortex
Benchmark（ Re=1500 AR=3 Ro=2.56）
^
Planetary vorticity tilting (PVT)
PVTr contributes to LEV stability by removing radial vorticity (Re>100)
Once established, the contribution of PVTr is almost Re-independent and time-invariant

## Slide 22
Vorticity Dynamics of Leading-edge Vortex
Benchmark（ Re=1500 AR=3 Ro=2.56）
^
Dual-stage radial-tangential vortex tilting
The mixing of radial and tangential vorticity within the stable LEV region

## Slide 23
Vorticity Dynamics of Leading-edge Vortex
Benchmark（ Re=1500 AR=3 Ro=2.56）
^
Dual-stage radial-tangential vortex tilting
The ratio of radial and tangential vorticity within the stable LEV results in a constant.
Any transform between radial vorticity and tangential vorticity?

## Slide 24
Vorticity Dynamics of Leading-edge Vortex
Benchmark（ Re=1500 AR=3 Ro=2.56）
^
Dual-stage radial-tangential vortex tilting
The mutual conversion between radial vorticity and tangential vorticity
Tilting of tangential vorticity component into radial direction
Tilting of radial vorticity component into tangential direction

## Slide 25
Vorticity Dynamics of Leading-edge Vortex
Benchmark（ Re=1500 AR=3 Ro=2.56）
^
Dual-stage radial-tangential vortex tilting
The Tr→t can enhance the (positive) tangential vorticity
Tangential velocity increases towards the wing tip
Located at the rear boundary of the LEV

## Slide 26
Vorticity Dynamics of Leading-edge Vortex
Benchmark（ Re=1500 AR=3 Ro=2.56）
^
Dual-stage radial-tangential vortex tilting
The Tt→r can cancel out negative radial vorticity in LEV
A reduction of tipward flow along the tangential direction is necessary
The Tt→r and Tr→t can build up a bidirectional transform of radial and tangential vorticity

## Slide 27
Vorticity Dynamics of Leading-edge Vortex
Benchmark（ Re=1500 AR=3 Ro=2.56）
^
Dual-stage radial-tangential vortex tilting
Tilting of tangential vorticity component into radial direction
Tilting of radial vorticity component into tangential direction
A negative feedback loop

## Slide 28
Vorticity Dynamics of Leading-edge Vortex
Conclusions and other works
^
The 3D vorticity transports during LEV formation until the steady state has been addressed
Two novel mechanisms for LEV stability has been presented.
Planetary vorticity tilting (PVT) and Dual-stage radial-tangential vortex tilting
The role of Coriolis acceleration in LEV stability has been explained from a vorticity transport perspective.
Effects of Re, AR, Ro and α…
More complicated wing motions, e.g., flapping, pitch-up, forward flight.

## Slide 29
Acknowledgment
Collaboration with Penn State
^
BioRob-InFL Lab
BEIHANG Group
Prof. B. Cheng
Prof. N.H. Werner
Prof. J.H.
Wu
Prof. C.
Zhou
Prof. J.J.
Wang
Prof. L.
Chen
Publications:
Chen, L. et al. (2023). Vorticity dynamics and stability of the leading-edge vortex on revolving wings. Physics of Fluids, 35(9), 091301.
Chen, L. et al. (2023). Dual-stage radial-tangential vortex tilting reverses radial vorticity and contributes to leading-edge vortex stability on revolving wings. Journal of Fluid Mechanics, A29, 963.
Chen, L. et al. (2022). Effects of Reynolds number on leading-edge vortex formation dynamics and stability in revolving wings. Journal of Fluid Mechanics, A31, 931.
Chen, L. et al. (2020). Leading-edge vortex formation and transient lift generation on a revolving wing at low Reynolds number. Aerospace Science and Technology, 97, 105589.
Chen, L. et al. (2019). Volumetric measurement and vorticity dynamics of leading-edge vortex formation on a revolving wing. Experiments in Fluids, 60, 1-15.