## Slide 1
Jen Beverly
Presented at BIRS Workshop Climate Change Scenarios and Financial Risk
July 5th, 2022
jen.beverly@ualberta.ca
wildfireanalytics.org
@fireanalytics
Connect
Characterizing biophysical wildfire processes for strategic risk assessment – Selected methods and considerations

## Slide 2
2
Wildfires can impact communities
  547 evacuation events
  497 homes destroyed
  209,121 evacuees
  Median number evacuated per year: 3,590
  Median number of homes lost 2
  Median distance from fire: 3 km
  Prompted by smoke: 19%
  Civilian fatalities 1
More people evacuated 2011-2018 than in the previous 31 years

## Slide 3
3
Trend or outliers?
Slave Lake 2011
May 2011
Fort McMurray 2016
May 2016
Lytton 2021
June 2021
(Photo sources: Andy Clark/Reuters; Town of Slave Lake; Twitter.com/Jerome Garot/EPA; Edith Loring-Kuhanga/Facebook)
August 2003
Kelowna 2003
70 km/h winds
1,000 evacuated
Village 90% destroyed
$78M insured damages
100 km/h winds
7,000 evacuated
433 homes destroyed
$700M insured damages
72 km/h winds
90,000 evacuated
2,400 homes destroyed
$3.6B insured damages
100 km/h winds
27,000 evacuated
239 homes destroyed
$200M in damages
Notes: 63 to 74 km/h - strong enough to send large, loose objects (garbage cans, patio furniture) flying. Tree limbs can break, cars can veer off the road.
By 75 km/h, the wind is strong enough to damage structures.
By 90 km/h it can uproot entire trees.

## Slide 4
4
June 30, 2021
May 3, 2016
May 15, 2011
>30
20-30
10-20
5-10
0-5
Nil
Fire Weather Index (FWI)
A numeric rating of fire intensity.
Used as general index of fire danger throughout the forested areas of Canada.
Map source: CWFIS, NRCan
August 22, 2003
Slave Lake
Fort McMurray
Lytton
Kelowna

## Slide 5
4
Illustration sources: Tank - O.Tasai; house – vecteezy.com
Perfect storm
fuels are available
AND
the wind blows towards me
AND
there’s an ignition
“the perfect storm” – when a confluence of many factors or events – no one of which alone is particularly devastating – creates a catastrophic force. Such confluence is rare and devastating (Emanuel and Fuchs 2008).
5

## Slide 6
4
Illustration sources: Tank - O.Tasai; house – vecteezy.com
Grey swan
fuels are available
AND
the wind blows towards me
AND
there’s an ignition
5
“grey swan” – known events with unknown likelihood (Nafday 2011); we can specify outcomes but not probabilities (Gholami et al. 2018); we are in a state of “incomplete” knowledge in which attempts to assign probabilities are neither rational nor science-based (Sterling 2007).
6

## Slide 7
7
Fuel characteristics (structure) matters
Amount of surface fuel
Amount and compactness of crown fuel
Crown base height
Fuels are the hazard (potential source of harm)

## Slide 8
8
Fire intensity dictates suppression effectiveness
  Ground
  Surface
  Crown
  Suppression success
  Suppression failures
Threshold for ground crew effectiveness
Threshold for airtanker effectiveness
I = h w r

## Slide 9
9
Where can we expect fires? Fixed versus variable factors
There are things we can know for today, the next several days
Fuel moisture (availability)
Wind speed, direction
Ignition agents
There are things we can know for this season, the next several seasons
What burns, where it is (fuel)
Operational capabilities
Location of values (receptors)
Highly variable within a fire season
(lots of predictive uncertainty)
Mostly fixed within a fire season
(lots of certainty)

## Slide 10
3
Threat rating
Number of fires per 4 km2 1950-1991
[ignition patterns]
Development; timber values; visual quality
Initial attack time; terrain; water proximity
Rate of spread; intensity; crown fraction burned
Wildfire threat map and four component maps of the Wildfire Threat Rating System for McGregor Model Forest
Source: Hawkes, B., Beck, J., 1997. A wildfire threat rating system. Forestry Canada, Pacific Forestry Centre, Technology Transfer Notes 1, Victoria, BC, Canada.
Wildfire Threat
Ignition patterns

## Slide 11
Spatial context – fires are contagious
11
Point estimate of a threat is detached from the spatial context of its surrounding fuel neighbourhood
Ignores the contagious nature of fires
Photo source: https://peakvisor.com/park/elk-island-national-park.html

## Slide 12
Solution? Simulate the spread of fires
12
C-2 Boreal Spruce
I = h w r
Rate of spread (n = 48)
Weight of fuel consumed (n = 13)
Constant – heat of combustion
Image source: N. McLoughlin

## Slide 13
Monte Carlo simulation process
Iteration 1
13
Many simulations - express fixed and variable factors

## Slide 14
Iteration 2
14
Many simulations - express fixed and variable factors
Monte Carlo simulation process

## Slide 15
Iteration 1
Iteration 2
Burn probability (BP) at a given pixel in the landscape grid is calculated as:
# times the pixel burned
# chances to burn (iterations)
BP = 1/2 or 0.5
BP = 2/2 or 1.0
15
Simulated burn probability

## Slide 16
Model climate change scenarios
17
Model inputs adjusted to reflect climate change scenarios (weather pools, escaped fire numbers)
Historical data used to calibrate model (duration of burning, spread event days)
Relies on historical ignition patterns
Relevance of historical data to current and future conditions questionable (occurred under different conditions)

## Slide 17
Stochasticity means thousands of iterations required
17
Base Case Replicate 1
Base Case Replicate 2
30% different
Replicate maps can differ from each other
To explore impacts of scenarios, modelers therefore fixed the fire sets by holding ignition points constant and then varying other inputs like the fuels or the weather

## Slide 18
18
2005 Burn Probability
Does it work?
Estimated with 2005 data
Published 2009
Slave lake burned 2011
2.4 million ha study are
25,000 iterations
125,000 simulated fires
Fox Creek
Whitecourt
Swan Hills
Slave Lake
Beverly et al. (2009)

## Slide 19
2011
2009
2006
2011
2011
2011
Burn Probability Class
19
Where did real fires burn?

## Slide 20
Do fires burn preferentially in BP hotspots? No.
5 study areas
138 fires
543,049 ha burned
70% of burned areas occurred in areas where burn probability was in the lower half of the range (i.e., in the BP cold spots)
20
Beverly and McLoughlin (2019)
Slave Lake
Fort McMurray

## Slide 21
Exposure based on transmission distances
500 m
30 m
100 m
Radiant Heat
Longer range embers
Shorter range embers
21
Beverly et al. (2009)

## Slide 22
7
Highway 88
22

## Slide 23
Simple metric of exposure (Beverly, McLoughlin, Chapman 2021)
500 m
Forest Protection Area land cover
100 m
100 m
23
There are 80 pixels within 500 m – how many can transmit fire to me?
Hazard Fuel (1)
Other land cover types (0)
  Σ hazard fuel pixels 75
  total pixels 80
94% exposure
= 0.94
=

## Slide 24
Exposure based on 2007 fuel map
Overlaid fires in the years that followed (2007-2019)
2,331 fires, burned 2,606,387 ha
burned area
protection area
Same validation test as BP simulation
study area
Landscape fire exposure –
a numeric rating of the potential for fire transmission to a location given surrounding fuel composition and configuration, irrespective of weather or other fire controls.
24

## Slide 25
Forest Protection Area land cover
100 m
100 m
Tried weighting pixels by:
  Nearness
  Crown fuel load (CFL)
  Head fire intensity (HFI)
  Rate of spread (ROS)
Tried increasing window to 1000 m
Increased complexity did not improve correspondence with real fires
25
Hazard Fuel (1)
Other land cover types (0)
What about weighting for distance, CFL, HFI, ROS?

## Slide 26
Can be combined with variable fire controls
Exposure (%)
Receptive and exposed
26
Landscape fire exposure –
a numeric rating of the potential for fire transmission to a location given surrounding fuel composition and configuration, irrespective of weather or other fire controls.

## Slide 27
27
PhD student Air Forbes
Metrics for characterizing wildfire exposure around communities
Identify community exposure types/groups
PD – Number of Patches
CV – Patch Size Coefficient of Variation
CA – Class Area
Next steps
Lake Louise
Whitecourt

## Slide 28
Thank you, looking forward to questions and discussion
Jen Beverly
jen.beverly@ualberta.ca
wildfireanalytics.org
@fireanalytics
Connect
Acknowledgements
Alberta Wildfire
  Neal McLoughlin
  Liz Chapman
  Laura Stewart
Forest Resource Improvement Association of Alberta (FRIAA)
Institute for Catastrophic Loss Reduction (ICLR)
28