## Slide 1: Routing vs Network Coding and Combinatorial Optimization
Chandra Chekuri
Univ. of Illinois @ Urbana-Champaign

## Slide 2: Coding Advantage
Question: What is the advantage/benefit/gain of network coding in improving throughput?

## Slide 3: Coding Advantage
Question: What is the advantage/benefit/gain of network coding in improving throughput?
Survey known quantitative bounds in a two basic scenarios: multicast and multiple unicast
Highlight connections to results/questions/ideas in combinatorial optimization
Some open problems

## Slide 4: Multicast Example
S
R1
R2
b1
b2
b1
b2
b1
b2
b1+b2
b1+b2
b1+b2
S can multicast to R1 and R2 at rate 2
using network coding
[Ahlswede-Cai-Li-Yeung]

## Slide 5: Multicast Example
S
R1
R2
b1
b2
b1
b2
b1
b2
b1+b2
b1+b2
b1+b2
S can multicast to R1 and R2 at rate 2
using network coding
Optimal rate since
min-cut(S, R1) = min-cut(S, R2) = 2
[Ahlswede-Cai-Li-Yeung]

## Slide 6: Multicast Example
S
R1
R2
b1
b2
b1
b2
b1
b2
b1+b2
b1+b2
b1+b2
S can multicast to R1 and R2 at rate 2
using network coding
Optimal rate since
min-cut(S, R1) = min-cut(S, R2) = 2
Question: what is the best achievable rate without coding (only routing) ?

## Slide 7: Multicast Example
S
R1
R2
b1
b1
b1
S can multicast to R1 and R2 at rate 2
using network coding
Optimal rate since
min-cut(S, R1) = min-cut(S, R2) = 2
Question: what is the best achievable rate without coding (only routing) ?
Rate 1 is easy
Can we do better?
b1

## Slide 8
Question: what is the best achievable rate without coding?
Rate 1 is easy. Can we do better?
Yes, in a fractional sense
T1 , T2 , T3 are multicast/Steiner trees: each edge of G in at most 2 trees
Use each tree for ½ the time. Rate = 3/2
R2
R2
S
R1
T3
S
R1
T1
S
R1
R2
T2

## Slide 9
S
R1
R2
b1
b2
b1
b1
b1
b1
S
b3
b3
b3
b2
b2
b2
b2
b3
3 bits in 2 time units
R1
R2
R2
R2
S
R1
T3
S
R1
T1
S
R1
R2
T2

## Slide 10: Packing Steiner trees
Definition: Given graph G=(V,E), root node S and terminals/receiver nodes R1, ..., Rk a multicast/Steiner tree is an out-tree T rooted at S that contains a path from S to each receiver Ri
T set of all Steiner trees in G for S and R1, ..., Rk
Definition: A packing of Steiner trees is an assignment of non-negative numbers xT for each T in T such that Σe in T xT ≤ ce for each edge e of G. The value of the packing is ΣT xT
ce : capacity of e

## Slide 11: Packing Steiner trees: LP
T set of all Steiner trees in G for S and R1, ..., Rk
Definition: A packing of Steiner trees is an assignment of non-negative numbers xT for each T in T such that Σe in T xT ≤ ce for each edge e of G. The value of the packing is ΣT xT
max ΣT xT
s.t
ΣT: e in T xT ≤ ce for all e
xT ≥ 0 for all T

## Slide 12: Coding Advantage for Multicast in Dir Graphs
Given graph G=(V,E), source S and receivers R1, ..., Rk
rc : multicast rate with coding
r : multicast rate without coding (aka routing)
rc / r : coding advantage
what is the ratio rc / r for the given instance? can it be computed?
what is the worst case value of rc / r over all inputs as a function of k and the graph size?

## Slide 13: Multicast in Dir Graphs
rc : multicast rate with coding
[Ahlswede-Cai-Li-Yeung]
Theorem: rc = mini mincut(S,Ri) and can be computed in polynomial time
r : multicast rate without coding (aka routing)
[Sanders etal, Li etal ]
Proposition: r is the value of the maximum Steiner tree packing in G for S and R1, ..., Rk
NP-hard to compute r [Jain-Mahdian-Salavatipour]

## Slide 14: Multicast in Dir Graphs
what is the ratio rc / r for the given instance? can it be computed?
NP-hard 
what is the worst case value of rc / r over all inputs as a function of k and the graph size?
[Agarwal-Charikar]
Theorem: Worst case value of rc / r is exactly equal to the worst case integrality gap of the natural LP relaxation for the min-weight Steiner tree problem

## Slide 15: Multicast in Dir Graphs
[Agarwal-Charikar]
Theorem: Worst case value of rc / r is exactly equal to the worst case integrality gap of the natural LP relaxation for the min-weight Steiner tree problem
Known integrality gap results for directed Steiner tree
k: # of terminals/receivers, n: # of nodes in G
g* ≤ k , trivial
g* ≥ c (log n/ log log n)2 [Halperin etal]
g* ≥ c √k [Zosin-Khuller]
g* = O(polylog(n)) ? important open problem!

## Slide 16: Multicast in Undir Graphs
[Agarwal-Charikar]
Theorem: Worst case value of rc / r is exactly equal to the worst case integrality gap of the bi-directed LP relaxation for the min-weight Steiner tree problem
Known gap results on bi-directed LP for Steiner tree
g* ≤ 2 several proofs
g* ≥ 8/7 [Goemans]
Precise value of g* ? important open problem!

## Slide 17: Multicast in Undir Graphs
What is an undirected graph in terms of transmission?
Model: undir edge uv with capacity c can be replaced by two dir edges (u,v) and (v,u) with capacities c1 and c2 such that c1 + c2 = c
u
v
c
u
v
c1
c2

## Slide 18: Multicast in Undir Graphs
[Li etal]
Theorem: Given undir G, source S and R1, ..., Rk, rc can be computed in polynomial-time via a linear program
Bi-direct edges of G to maximize min-cut from S to R1, ..., Rk in the resulting directed graph
[Agarwal-Charikar] rely on above LP for connecting to the bi-directed relaxation for undir Steiner tree

## Slide 19: Proof Outline
[Agarwal-Charikar]
Theorem: Worst case value of rc / r is exactly equal to the worst case integrality gap of the natural LP relaxation for the min-weight Steiner tree problem
General principle: Packing and optimization via LP duality and equivalence of optimization and separation (ellipsoid method)

## Slide 20: Min-weight Steiner tree
Input: G=(V,E), source S, terminals R1,..,Rk. Edge e has weight we
Goal: Output min-weight Steiner tree (rooted at S and has paths to each terminal)
NP-Hard and hard to approximate in undirected and directed graphs

## Slide 21: LP for Steiner tree
Input: G=(V,E), source S, terminals R1,..,Rk. Edge e has weight we
Goal: Output min-weight Steiner tree (rooted at S and has paths to each terminal)
min Σe we ze
s.t
Σe in δ(A) ze ≥ 1 for all valid A  V
ze ≥ 0 for all e
A
S

## Slide 22: LP for Steiner tree
Input: G=(V,E), source S, terminals R1,..,Rk. Edge e has weight we
Goal: Output min-weight Steiner tree (rooted at S and has paths to each terminal)
min Σe we ze
s.t
Σe in δ(A) ze ≥ 1 for all valid A  V
ze ≥ 0 for all e
A
S
z : capacities on edges s.t min-cut(S, Ri) ≥ 1 for all i

## Slide 23: LP for Steiner tree
Integrality gap: g = maxI OPT(I) / OPT-LP(I)
min Σe we ze
s.t
Σe in δ(A) ze ≥ 1 for all valid A  V
ze ≥ 0 for all e
A
S

## Slide 24: LP for Steiner tree
Integrality gap: g = maxI OPT(I) / OPT-LP(I)
There is an instance g = OPT(I) / OPT-LP(I)
min Σe we ze
s.t
Σe in δ(A) ze ≥ 1 for all valid A  V
ze ≥ 0 for all e
A
S

## Slide 25: LP for Steiner tree
Integrality gap: g = maxI OPT(I) / OPT-LP(I)
There is an instance g = OPT(I) / OPT-LP(I)
I = (G,S,R), z be an optimum solution to LP
Wlog, by scaling weights, assume that OPT(I) = 1 and hence OPT-LP(I) = 1/g = Σe we ze
min Σe we ze
s.t
Σe in δ(A) ze ≥ 1 for all valid A  V
ze ≥ 0 for all e

## Slide 26: Back to Coding Advantage
Want to use (G,S,R) and z to show that
coding-advantage = rc (G,S,R,z) / r(G,S,R,z) ≥ g
rc (G,S,R,z) = network coding rate with capacities z
r(G,S,R,z) = rate with capacities z without coding
Properties of (G,S,R,z):
for any Steiner tree T, w(T) ≥ 1
we ze = 1/g

## Slide 27: Back to Coding Advantage
rc (G,S,R,z) = network coding rate with capacities z
r(G,S,R,z) = rate with capacities z without coding
Claim: rc (G,S,R,z) ≥ 1
Since z is feasible for Steiner-LP, for each Ri,
min-cut(S,Ri) ≥ 1 in graph with capacities set to z

## Slide 28: Back to Coding Advantage
rc (G,S,R,z) = network coding rate with capacities z
r(G,S,R,z) = rate with capacities z without coding
Claim: rc (G,S,R,z) ≥ 1
Main Claim: r(G,S,R,z) = 1/g

## Slide 29: Proof of Main Claim
r(G,S,R,z) = rate with capacities z without coding
Main Claim: r(G,S,R,z) = 1/g
r(G,S,R,z) is max value of a Steiner tree packing in G with capacities set to z
Can pack only 1/g Steiner trees into z

## Slide 30: Proof of Main Claim
r(G,S,R,z) is max value of a Steiner tree packing in G with capacities set to z
r = max ΣT xT
s.t
ΣT: e in T xT ≤ ze for all e
xT ≥ 0 for all T
r = min Σe ze ye
s.t
Σe in T ye ≥ 1 for all T
ye ≥ 0 for all e
Primal LP
Dual LP

## Slide 31: Proof of Main Claim
r = min Σe ze ye
s.t
Σe in T ye ≥ 1 for all T
ye ≥ 0 for all e
Claim: r ≤ 1/g
Proof:
Set ye = we for each e
Properties of (G,S,R,z):
for any Steiner tree T, w(T) ≥ 1
we ze = 1/g
min Σe we ze
s.t
Σe in δ(A) ze ≥ 1 for all valid A  V
ze ≥ 0 for all e

## Slide 32: Multicast: other results
[Kiraly-Lau] Coding advantage is at most 2 in hypergraphs. Relies on a new orientation theorem for hypergraphs
[C-Soljanin-Fragouli] Coding advantage is at most 2 for undirected non-uniform multicast. Relies on a Steiner tree packing theorem of [BangJensen-Frank-Jackson].
[C-Soljanin-Fragouli] Coding advantage for average throughput is also related to the integrality gap of Steiner trees. Large for directed graphs
[Goel-Khanna] Coding advantage (in terms of power) is O (1) for wireless transmission in Euclidean space

## Slide 33: Multicast Summary
Coding advantage is large in directed graphs and small in undirected/symmetric graphs. NP-Hard to compute for a given instance.
Coding advantage is closely related to various aspects of the Steiner tree problem.

## Slide 34: Multiple Sessions/Sources
k independent sessions sharing a network G
Session i has source Si and receiver set Ri (each sessions is a multicast)
Session i has a demand di
R1
S1
S2
R2

## Slide 35: Multiple Unicast/k-pairs problem
k independent sessions sharing a network G
Session i has source Si and single receiver Ti
Session i has a demand di
T1
S1
S2
T2

## Slide 36: Multiple Unicast (k-pairs problem)
k independent sessions sharing a network G
Session i has source Si and single receiver Ti
Session i has a demand di
Rate region: all vectors (r1, r2, ..., rk) such that rate of ri di for (Si, Ti) is simultaneously achievable in G
Max concurrent rate: max r such that rate r di is for (Si, Ti) is simultaneously achievable in G

## Slide 37: Multiple Unicast
k independent sessions sharing a network G
Session i has source Si and single receiver Ti
Session i has a demand di
Rate region: all vectors (r1, r2, ..., rk) such that rate of ri di for (Si, Ti) is simultaneously achievable in G
Max concurrent rate: max r such that rate r di is for (Si, Ti) is simultaneously achievable in G

## Slide 38: Coding Advantage
Given G, k pairs (S1,T1), ..., (Sk,Tk) and demands d1,...,dk
rc : max value such that G supports rc di simultaneously for each i with coding
r : max value G supports r di simultaneously for each i without coding

## Slide 39: Understanding r and rc
r = max concurrent multi-commodity flow
Can be computed in poly-time via linear programming
rc : no known exact characterization. Computability is open? difficult open problem
Goal: bounds on rc / r via bounds on rc and r

## Slide 40: Understanding r
r = max concurrent multi-commodity flow
T1
S1
S2
T2
o.3
o.5
o.2
0.5
0.5

## Slide 41: Understanding r
r = max concurrent multi-commodity flow
fie : flow on edge e for pair/commodity i
max r
s.t
Σe out of Si fie ≥ r di for all i
Σe out of v fie = Σe in to v fie for all i, v not in {Si,Ti}
Σi fie ≤ ce for all e
xT ≥ 0 for all T

## Slide 42: Understanding r
r = max concurrent multi-commodity flow
T1
S1
S2
T2
r = 1/2

## Slide 43: Sparsity
Definitions:
For graph G=(V,E) and an edge set A separates u from v if (V,E-A) has no path from u to v
For edge set A, dem-sep(A) = sum of demands of all pairs (Si,Ti) separated by A
Sparsity(A) = cap(A)/dem-sep(A)
min-sparsity = minA Sparsity(A)

## Slide 44: Sparsity
min-sparsity = minA Sparsity(A)
T1
S1
S2
T2
e
min-sparsity = sparsity({e})= 1/2

## Slide 45: Sparsity and r
Proposition: For dir and undir graphs, r ≤ min-sparsity
T1
S1
S2
T2
e
min-sparsity = sparsity({e})= 1/2

## Slide 46: Sparsity and rc
Proposition: For dir and undir graphs, r ≤ min-sparsity
Example shows that rc = 1 > min-sparsity [Ahlswede etal]
T1
S1
S2
T2
Ahlswede etal
e
min-sparsity = sparsity({e})= 1/2
b1
b2
b1
b2
b1 + b2
b1 + b2
b1 + b2

## Slide 47: Coding Advantage in Dir Graphs
[Harvey-Kleinberg-Lehman]
Exists a dir graph instance such that
k = Θ(n) = Θ(m)
r ≤ min-sparsity = O(1/k)
rc = 1
Recursive construction building on previous example
Implication: coding advantage = Ω(k)
Note that for all instances rc / r ≤ k

## Slide 48: Coding Advantage in Undir Graphs
[Harvey etal][Jain etal] [Kramer-Savari]
Lemma: For undirected graphs, r ≤ rc ≤ min-sparsity

## Slide 49: Coding Advantage in Undir Graphs
[Harvey etal][Jain etal] [Kramer-Savari]
Lemma: For undirected graphs, r ≤ rc ≤ min-sparsity
Why is it true in undir graphs and not in dir graphs?
Intuition: In undir graphs the min-sparse cut partitions V into (X, V-X). Not true in dir graphs.
X
V-X

## Slide 50: Coding Advantage in Undir Graphs
[Harvey etal][Jain etal] [Kramer-Savari]
Proposition: For undirected graphs, r ≤ rc ≤ min-sparsity
min-sparsity / r is called the flow-cut gap
Coding advantage = rc / r ≤ flow-cut gap

## Slide 51: Coding Advantage in Undir Graphs
Coding advantage = rc / r ≤ flow-cut gap
Large literature on flow-cut gaps in undirectd graphs
gap = 1 for k = 2 [Hu]
gap = 1 for special cases (see [Schrijver book])
gap = O(log k) for all instances [Linial,London,Rabinovich]
gap = O(√log k) for planar and minor-free graphs [Ra0]
Conjecture: gap = O(1) for planar and minor-free graphs [Gupta,Neman-Rabinovich,Sinclair]

## Slide 52: Coding Advantage in Undir Graphs
[Li-Li] and others
Bold Conjecture: rc = r for all undir graph multiple unicast instances!
No advantage if conjecture is true!

## Slide 53: Coding Advantage in Undir Graphs
Remark: Flow-cut gap ideas can be extended to bound coding advantage for multiple sessions/multicast case to be O(log n)
Related to the Steiner ratio cut problem and the integrality gap of its LP relaxation

## Slide 54: Coding Advantage for Multiple Unicast: Summary
Coding advantage very large for directed graphs
Coding advantage is at most the flow-cut gap in undirected graphs. Conjectured to be 1
Wide open: (approximate) understanding of rc
  Several upper bounds based on generalizations of cuts and other information inequalities

## Slide 55: Conclusions
Coding advantage large in directed graphs
Much less in undirected graphs
  at most 2 a for multicast
  at most flow-cut gap for mult. unicast; O(log k)
  at most Steiner ratio gap for mult. multicast; O(log n)
Several (difficult) open problems in resolving precise bounds on coding advantage