## Slide 1: Stochastic Modelling of Extreme Precipitation – From Global Scale to Urban Scale
Dr. Chandra R. Rajulapati
University of Saskatchewan
Retreat for Young Researchers in Probability and Areas of Application
Sep. 28, 2019
Banff International Research Station, Banff

## Slide 2: Overview
A little background about me
Introduction to modelling precipitation
Global scale – uncertainties
Regional scale – hydrological modelling
Urban scale – how different are uncertainties?
Conclude - a few insights and challenges ahead
Source: Google images

## Slide 3: A little background about me
PIMS-GWF Postdoctoral fellow (Nov. 2018 – Nov. 2020) – a joint fellowship – Working with Prof. John Pomeroy, Dr. Saman Razavi, and Dr. Simon Papalexiou
Doctoral Degree from IISc, Bangalore, India (2012-2017)
Work experience
Hydel power plants
High rise buildings
Postdoctoral Researcher, Indian Institute of Science (IISc), Bangalore, India (2017-2018)

## Slide 4: Introduction
Precipitation – most important variable – high spatial variability and intermittency
Involves complicated processes
Pretty confident with Halley’s comet coming close to earth, but difficult to say what is the average precipitation in the next month
Source: https://www.sciencedirect.com/topics/earth-and-planetary-sciences/hydrologic-cycle

## Slide 5: Introduction
Yet we have decisions to take:
  design a dam or a levee
  Construct an urban drainage system
  Predict areas probable to flood
Stochastic modelling is one among other methods
History provides valuable clue to the future!
Model the statistical parameters of historical time series
Notes: We have gauges measuring the precipitation, use the measurements

## Slide 6: Introduction
Intensity – Duration – Frequency (IDF) relationships
Chart: Duration (hours)
| 24 | 12 | 6 | 3 | 1 | 0.5 | 0.25
2 Year | 3.0993 | 5.7298 | 10.3823 | 19.0495 | 43.4659 | 70.006 | 91.7927
5 Year | 4.1477 | 7.6984 | 14.0598 | 25.8409 | 54.8832 | 87.9012 | 114.3802
10 Year | 4.891 | 9.0898 | 16.7001 | 30.6155 | 61.1795 | 98.1038 | 128.493
25 Year | 5.8902 | 10.9551 | 20.2901 | 36.9848 | 67.9363 | 109.3802 | 145.4191
50 Year | 6.6772 | 12.4206 | 23.1496 | 41.9654 | 72.2081 | 116.7195 | 157.3541
100 Year | 7.4993 | 13.9479 | 26.1648 | 47.1354 | 75.9122 | 123.2411 | 168.702
Return period () is the expected value of recurrence interval or the time between occurrences
10-year return level is 180 mm/hr
  The probability that the intensity will equal or exceed 180 mm/hr in any year is approximately 0.1 (1/10).
Notes: Return period is the average recurrence interval between events equaling or exceeding a specified magnitude.

## Slide 7: Introduction
Useful for predictions - a dam or levee may be designed for 1000-year return levels, spillways for 10,000-year, urban drainage for 5-year
Calculate projected return levels
  Minimum of 30 years of data.
Rain gauge data – major source of data
Do we have enough gauge data?

## Slide 8: Global Scale
Daily gauges
Min 30 years of data
With less than 20% data gaps

## Slide 9: Gridded precipitation products
Datasets based on observations
Other than Rain gauges
Satellites
Reanalysis
  merge irregular observations and models that encompass many physical and dynamical processes in order to generate a synthesized estimate of the state of the system – precipitation is an output
Source: Sun et al., 2018
Notes: The idea behind reanalysis systems is to merge irregular observations and models that encompass many phy-sical and dynamical processes in order to generate a synthesized estimate of the state of the system across auniform grid, with spatial homogeneity, temporal continuity, and a multidimensional hierarchy.

## Slide 10: Gridded precipitation products
Assimilated data products: MSWEP (Multi-Source Weighted-Ensemble Precipitation)
Source: Sun et al., 2018

## Slide 11: Gridded precipitation products
Modelling extreme precipitation – Global scale
Several ways to draw an extreme sample
Annual maxima or threshold maxima follows GEV and GPD resp., following extreme value theory
Number of extremes equal to the
number of years
Tail sample (typically 1%, 5% extremes)
Here we consider 5% of tail sample and fit two types of tails – Power type and exponential

## Slide 12: Gridded precipitation products
The tail functions of the Pareto II and Weibull distributions are given, resp, by
where γ and β are shape (or the tail index) and scale parameters, respectively
Estimates of parameters by fitting the theoretical tails to the empirical ones by minimizing the Probability Root Mean Square Error (PRMSE) norm
where n is the tail sample size, is the exceedance probability of corresponding to the theoretical tail, i.e., PII or W, and is the empirical exceedance probability (according to the Weibull plotting position)

## Slide 13: Gridded precipitation products
Pareto II
Multi-Source Weighted-Ensemble Precipitation (MSWEP)

## Slide 14
Pareto II

## Slide 15: Gridded precipitation products
High value of tail index may not necessarily mean high precipitation
Brazilian and African tropical forests typically receive high precipitation, but this is consistent throughout the observation period we considered, and therefore a light tail is noticed.
Desert parts of Africa and rangelands of Australia, where a heavy tail is observed, one can expect extreme events much larger than the average precipitation.
Understanding tail behaviour helps in better preparedness in facing the extreme precipitation events, which always pose challenge to the society

## Slide 16: Gridded precipitation products
Pareto II
Multi-Source Weighted-Ensemble Precipitation (MSWEP)

## Slide 17: Gridded precipitation products
High value of tail index may not necessarily mean high precipitation
Brazilian and African tropical forests typically receive high precipitation, but this is consistent throughout the observation period we considered, and therefore a light tail is noticed.
Desert parts of Africa and rangelands of Australia, where a heavy tail is observed, one can expect extreme events much larger than the average precipitation.
Understanding tail behaviour helps in better preparedness in facing the extreme precipitation events, which always pose challenge to the society

## Slide 18: Uncertainty with datasets
Dataset name | Temporal resolution | Spatial resolution | Data source
National Centers for Environmental Prediction -Climate Forecast System Reanalysis (CFSR) | sub-daily (1979-2017) | 0.5 deg (Global) | Reanalysis
Multi-Source Weighted-Ensemble Precipitation (MSWEP) | Daily (1979-2016) | 0.5 deg (Global) | Observations Satellite Reanalysis
Climate Prediction Center Unified Gauge-Based Analysis of Global Daily Precipitation (CPC) | Daily (1979-2017) | 0.5 deg (Land) | Observations
Precipitation Estimation from Remotely Sensed Information using Artificial Neural Networks (PERSIANN) Climate Data Record | sub-daily (1983-2017) | 0.25 deg (60S – 60N) | Observations Satellite
WATCH Forcing Data ERA-Interim (WFDEI) corrected using Global Precipitation Climatology Centre | Daily (1979-2016) | 0.5 deg (Land) | Observations Reanalysis

## Slide 19: Uncertainty with datasets
CFSR
MSWEP
CPC
PERSIANN
WFDEI

## Slide 20: Uncertainty with datasets

## Slide 21: Uncertainty with datasets
Comparison of empirical (blue) and calculated return levels using Pareto II (orange) and Weibull (green) for T-year return period (T=39 years for CPC and CFSR; 38 years for MSWEP and WFDEI; 35 years for PERSIANN) at global and continental scale.
Empirical return levels are the maximum of observed precipitation.
Whiskers denote the 95% empirical confidence interval

## Slide 22: Uncertainty with datasets
Predicted 100- and 1000-year return levels using both Pareto-II (orange) and Weibull (green) distributions at global and continental scale.
The left side and right side of the plot shows 100-year and 1000-year return period respectively.

## Slide 23: Comparison with InSitu observations

## Slide 24: 100-year return levels

## Slide 25: Points to remember
The degree of discrepancy varies from region to region, with low differences in NA and Europe, and huge differences in Africa and SA.
Returns levels underestimated by the satellite-based PERSIANN and overestimated by the reanalysis-based CFSR, when compared with CPC and InSitu
In mid and high latitudes, while the other products show medium to heavy tails, the satellite-based PERSIANN indicate light tails
The reanalysis datasets, CFSR and WFDEI, differ substantially in their spatial patterns in tropics - possible reason for this difference could be that the simulated precipitation extremes are effected by the parameterizations of deep convection
Ground bases observations – very very important – unfortunately number of gauges have been reducing may be due to increasing operational and staffing costs associated with ground-based data collection, restrictions on the release of the data by NMA etc.

## Slide 26: Regional Scale
Typically precipitation modelling is same as global scale
At regional scale we are more interested in understanding how precipitation is affecting streamflow
Use a hydrological model
Gridded precipitation products are useful
Now we know which product is good for a region

## Slide 27: Hydrological modelling - MESH
MESH (Modélisation Environnementale communautaire - Surface Hydrology) is the hydrology land-surface scheme (HLSS) of Environment and Climate Change Canada's (ECCC's) community environmental modelling system
Water balance
grouped response unit (GRU) watershed delineation concept
Source: Zhang et al., 2018

## Slide 28: Hydrological modelling - MESH
Bow River Basin – above Calgary

## Slide 29: Hydrological modelling
1
2
3
4
5
6
7
8
9
10
11
12
A
B
C

## Slide 30: Points to remember
Precipitation has heavier tail than streamflow
Grids with urban GRUs have higher peaks compared to other GRUs
Similar behaviour in the mountains? But model shows different results

## Slide 31: Urban Scale
t
Q
After Urbanization
Before Urbanization
Urbanization alters hydrologic response of catchment
  Increase in volume of runoff
  Peak flow increases
  Time to peak increases
Important in urban flooding studies
https://sites.google.com/view/itraiufm/home?authuser=0

## Slide 32: Different uncertainty issues
Gridded products not an option anymore
Rely on InSitu observations
Short-duration (hourly to sub-hourly) time scales
Case study – Bangalore – one of the major cities in India
Notes: More than 30 years of data

## Slide 33: Case study – Bangalore city
Rain gauge measuring data at 15 min interval
Annual maximum series (AMS) is prepared for durations 15 min, 30 min, 1 hour, 3 hour etc.
Generalized extreme value (GEV) distribution
Return levels are obtained for return periods 2, 5, 10, 25, 50 and 100 year using

## Slide 34: Parameter Uncertainty
Estimates of GEV parameters
Maximum Likelihood Method (MLE)
Bayesian analysis

## Slide 35: Parameter Uncertainty
pdf of annual maximum precipitation (X) given the parameter vector ()
Unnormalized posterior density of the parameters is given by
 is the parameter vector
is the prior distribution of parameters

## Slide 36: Parameter Uncertainty
Probability density function (pdf) of 10-year return levels (mm/hr) for various durations in comparison with return levels from Maximum Likelihood Estimation (MLE) method
Pdf of return levels for 15-min duration at different return periods in comparison with return levels obtained from MLE method.
2-year
5-year
10-year
25-year
50-year
100 year
24 hour
12 hour
6 hour
3 hour
1 hour
30 min
15 min

## Slide 37: Parameter Uncertainty
Bayesian
Classical
Duration | Classical Approach |  | Bayesian Approach | 
 | Mean | Variance | Mean | Variance
15 min | 128.48 | 65.56 | 131.80 | 76.94
30 min | 98.1 | 32.62 | 100.97 | 51.32
12 hour | 9.09 | 0.73 | 9.25 | 0.65
24 hour | 4.89 | 0.21 | 4.95 | 0.18
*All units in mm/hr
Probabilistic IDF relationships for 10-year return period

## Slide 38
General Circulation Models (GCMs):
Tools for simulating time series of climate variables globally, accounting for effects of greenhouse gases in the atmosphere.
can simulate largescale circulation patterns (e.g., pressure and geo potential heights) well
do not reproduce well nonsmooth fields such as precipitation.
Climate models are systems of differential equations based on the basic laws of physics, fluid motion, and chemistry. To “run” a model, scientists divide the planet into a 3-dimensional grid, apply the basic equations, and evaluate the results. Atmospheric models calculate winds, heat transfer, radiation, relative humidity, and surface hydrology within each grid and evaluate interactions with neighboring points.
Projected IDF Relationships
https://www.ipcc-data.org/guidelines/pages/gcm_guide.html

## Slide 39
Projected IDF Relationships
https://www.ipcc.ch/

## Slide 40
GCM model with future climate scenarios and latitude-longitude
Model Name | Latitude | Longitude | Abbreviation | Climate Scenarios
ACCESS1_0 | 12.5 N | 76.875 E | A1 | RCP 4.5, RCP 8.5
BCC-CSM1-1 | 12.55 N | 78.75 E | BC1 | RCP 2.6, RCP 4.5, RCP 6.0, RCP 8.5
BCC-CSM1-1-M | 12.89 N | 77.6 E | BC1M | RCP 2.6, RCP 4.5, RCP 6.0, RCP 8.5
BNU-ESM | 12.55 N | 78.75 E | BNU | RCP 2.6, RCP 4.5, RCP 8.5
CanESM2 | 12.55 N | 78.7 E | CAN | RCP 2.6, RCP 4.5, RCP 8.5
CCSM4 | 12.7225 N | 77.5 E | C4 | RCP 2.6, RCP 4.5, RCP 6.0, RCP 8.5
CMCC-CMS | 12.1 N | 76.8 E | CMS | RCP 4.5, RCP 8.5
CNRM-CM5 | 11.9 N | 77.34 E | CN5 | RCP 4.5, RCP 8.5
CSIRO-MK3-6-0 | 12.12 N | 76.875 E | CM60 | RCP 2.6, RCP 4.5, RCP 6.0, RCP 8.5
FGOALS-G2 | 12.55 N | 78.75 E | FG2 | RCP 2.6, RCP 4.5, RCP 8.5
FGOALS-S2 | 12.4 N | 75.9 E | FS2 | RCP 2.6, RCP 4.5, RCP 6.0, RCP 8.5
GFDL-CM3 | 13 N | 78.75 E | GF3 | RCP 2.6, RCP 6.0
GFDL-ESM2G | 13.14 N | 76.25 E | GF2G | RCP 2.6, RCP 4.5, RCP 6.0, RCP 8.5
GFDL-ESM2M | 13.14 N | 76.25 E | GF2M | RCP 2.6, RCP 4.5, RCP 6.0, RCP 8.5
GISS-E2-R | 13 N | 76.25 E | GISS | RCP 4.5
HadGEM2-CC | 12.5 N | 76.87 E | HADC | RCP 4.5, RCP 8.5
HadGEM2-ES | 12.5 N | 76.875 E | HADE | RCP 2.6, RCP 4.5, RCP 6.0, RCP 8.5
INMCM4 | 12.75 N | 78 E | IN4 | RCP 4.5, RCP 8.5
IPSL-CM5A-LR | 12.31 N | 78.75 E | IPCL | RCP 2.6, RCP 4.5, RCP 6.0, RCP 8.5
IPSL-CM5A-MR | 12.6 N | 77.5 E | IPCM | RCP 2.6, RCP 4.5, RCP 6.0, RCP 8.5
MIROC5 | 11.9 N | 78.75 E | MI5 | RCP 2.6, RCP 4.5, RCP 6.0, RCP 8.5
MIROC-ESM-CHEM | 12.55 N | 78.75 E | MIEC | RCP 2.6, RCP 4.5, RCP 6.0, RCP 8.5
MIROC-ESM | 12.55 N | 78.75 E | MIE | RCP 2.6, RCP 4.5, RCP 6.0, RCP 8.5
MPI-ESM-LR | 12.12 N | 78.75 E | MPI | RCP 2.6, RCP 4.5, RCP 6.0, RCP 8.5
MRI-CGCM3 | 12.89 N. | 77.62 E | MRI | RCP 2.6, RCP 4.5, RCP 6.0, RCP 8.5
NorESM1-M | 12.31 N | 77.5 E | NEM | RCP 2.6., RCP 4.5, RCP 6.0, RCP 8.5
Model Uncertainty

## Slide 41
Annual precipitation from 26 GCMs. Mean precipitation across all GCMs (MEAN) and the observed gauge data (OBS) are also shown
RCP 2.6: 20, RCP 4.5: 25, RCP 6.0: 16 and RCP 8.5: 24 GCMs
Model Uncertainty
Precipitation (mm)
Three time slices: 2021-2050; 2051-2080; 2071-2100
Notes: 2021-2100 for three time slices, near future to far future

## Slide 42
Reliability Ensemble Averaging (REA)
Model performance criterion:
CDF deviations between the observed data and GCM projected precipitation for control period
Model convergence criterion:
CDFs deviation for all GCMs for projected period from the weighted mean CDF.
GCM-Model Name | RCP2.6 2021-2050 | RCP2.6 2051-2080 | RCP2.6 2071-2100
BCC-CSM1-1 | 0.037 | 0.049 | 0.148
BCC-CSM1-1-M | 0.056 | 0.023 | 0.031
BNU-ESM | 0.042 | 0.038 | 0.030
CanESM2 | 0.046 | 0.056 | 0.098
CCSM4 | 0.033 | 0.092 | 0.113
CSIRO-MK3-6-0 | 0.059 | 0.035 | 0.053
FGOALS-G2 | 0.032 | 0.024 | 0.029
FGOALS-S2 | 0.021 | 0.021 | 0.019
GFDL-CM3 | 0.040 | 0.035 | 0.038
GFDL-ESM2G | 0.032 | 0.020 | 0.029
GFDL-ESM2M | 0.071 | 0.028 | 0.022
HadGEM2-ES | 0.015 | 0.047 | 0.100
IPSL-CM5A-LR | 0.086 | 0.081 | 0.056
IPSL-CM5A-MR | 0.049 | 0.038 | 0.034
MIROC5 | 0.044 | 0.031 | 0.029
MIROC-ESM-CHEM | 0.025 | 0.070 | 0.021
MIROC-ESM | 0.030 | 0.080 | 0.028
MPI-ESM-LR | 0.128 | 0.021 | 0.042
MRI-CGCM3 | 0.036 | 0.028 | 0.028
NorESM1-M | 0.117 | 0.183 | 0.049
Model Uncertainty
Notes: Control period 1969-1998
Obtain mean GCM from weights of control period
Got the projections at daily scale

## Slide 43: Projected Probabilistic IDF Relationships
Variation in return levels for various durations in comparison with classical approach and historical time line for the near future
(2021–2050)
Cumulative distribution function (cdf) of return level for 15-min duration, for RCP 2.6 and RCP 8.5 scenarios, and for the future three time slices for a 10-year return period.

## Slide 44: Projected Probabilistic IDF Relationships
Uncertainty in 10-year return levels for near future (2021–50) for different GCMs, REA averaged, and the uncertainty in return levels for historical time period (1969–2003) for 15-min. duration, for RCP 8.5 Scenario.
Notes: difference in return levels from the classical approach and the Bayesian approach. The deviance being high for most of the GCMs, it is important that one should consider an ensemble of GCMs in obtaining the future projections

## Slide 45: Percentage change (between mean of return levels from Bayesian approach and classical approach) in return levels for different GCMs and different RCP scenarios
Scenario GCM | RCP 2.6 (2021-50) | RCP 4.5 (2021-50) | RCP 6.0 (2021-50) | RCP 8.5 (2021-50) | RCP 8.5 (2071-2100)
REA | 1.4 | 1.2 | 1.4 | 0.8 | 0.8
A1 | - | -7.9 | - | -0.4 | -1.8
BC1 | -1.4 | 4.2 | 35.0 | -34.9 | -41.8
BC1M | -5.7 | -6.9 | 70.7 | 36.0 | 27.2
BNU | -5.2 | 21.2 | - | -4.6 | 57.2
CAN | 8.6 | -13.1 | - | -20.8 | 3.4
C4 | 29.4 | -30.3 | 17.1 | 60.0 | 48.1
CN5 | - | 12.3 | - | -26.3 | -32.6
CM60 | -13.3 | -18.1 | 13.6 | 61.1 | 154.5
GF2G | -3.1 | -20.8 | 104.2 | 3.6 | -33.7
GF2M | 37.2 | 1.5 | 31.3 | -30.6 | -48.8
GISS | - | 20.5 | - | - | -
HADC | - | -44.8 | - | -39.9 | -56.7
HADE | -17.8 | 6.7 | 23.6 | -26.8 | 20.5
IN4 | - | 32.5 | - | 53.1 | 162.1
IPCL | -2.3 | 4.8 | 0.5 | -49.9 | -47.1
IPCM | 13.5 | 11.7 | 79.4 | 2.9 | -34.6
MI5 | -10.6 | -0.7 | 12.2 | 29.4 | 147.1
MIEC | 39.9 | 17.8 | 41.4 | 69.6 | 79.8
NEM | -10.3 | -0.4 | 22.1 | 15.1 | -26.9

## Slide 46
Flood Analysis – Storm water drainage
With 30% reduction in Runoff due to Rainwater Harvesting
Propose structural and non-structural measures
Fire personal deploy at the flooding site
Resiliency of system - time to get back to the normal situation

## Slide 47
Quantification of Uncertainty in Spatial Return Levels of Urban Precipitation Extremes
Notes: 1948-2002
Min-17 years, max-54 years
See th stations <2 km, max distance- 52 km

## Slide 48
Annual, summer and monsoon maximum daily precipitation values form 1948 onwards at the three pairs of stations
Introduction

## Slide 49
Quantification of Uncertainty in Spatial Return Levels of Urban Precipitation Extremes
Chart: Rainfall during July 24-30, 2016 in Bangalore Pilot Study Area
| 24 | 25 | 26 | 27 | 28 | 29 | 30
1024 | 3 | 9.5 | 39.5 | 25.5 | 18.5 | 98 | 1
2316 | 0 | 20 | 90.5 | 35 | 18 | 79 | 1
2355 | 0 | 33.5 | 56.5 | 44.5 | 17 | 93.5 | 1
2353 | 1 | 32 | 76.5 | 42.5 | 23.5 | 94 | 1
2357 | 0.5 | 3.5 | 53.5 | 61 | 29.5 | 72 | 1
2842 | 0 | 22 | 24.5 | 37.5 | 24.5 | 85.5 | 0.5
2359 | 0 | 18.5 | 54.5 | 69.5 | 17.5 | 81 | 1
2847 | 1
Notes: 1948-2002
Min-17 years, max-54 years
See th stations <2 km, max distance- 52 km

## Slide 50
 = (1, 2)
1 - parameters in the data layer (parameters of the GEV distribution)
2 - parameters in the process layer (parameters of latent spatial process).
Hierarchical Bayesian Analysis
Data layer
Process layer
Prior layer

## Slide 51
Data layer
Hierarchical Bayesian Analysis
Location and scale parameters as Gaussian process
Process layer
GP (mean, covariance)

## Slide 52
S.No. | Covariates | Short form
Geographic |  | 
1 | Elevation | elev
2 | Latitude | lat
3 | Longitude | lon
Climatological |  | 
4 | Mean Annual Precipitation | MAP
5 | Mean Summer Precipitation | MSP
6 | Mean Monsoon Precipitation | MMP
7 | Mean Difference (Tmax-Tmin) Annual Temperature | DAT
8 | Mean Difference (Tmax-Tmin) Summer Temperature | DST
9 | Mean Difference (Tmax-Tmin) Monsoon Temperature | DMP
Hierarchical Bayesian Analysis

## Slide 53
Prior layer
Regression parameters are set to follow uniform distribution
Variogram parameters are set to follow uniform distribution based on the maximum and minimum range and sill of the empirical variogram
  Unif (–,+)
,0  Unif(2,35) ,1  Unif(16,100)
,0  Unif(0.005,0.05) ,1  Unif(5,50)
Hierarchical Bayesian Analysis

## Slide 54
Case | Covariates | DIC
Annual | MMP, elev | 10409.69
 | DTA, elev | 10410.18
Summer | MSP, elev | 9888.81
 | DTS, elev | 9889.62
Monsoon | lon, lat | 10405.87
 | elev | 10406.63
Summer maximum
Monsoon maximum
Annual maximum
Results

## Slide 55
Return level maps for 10 year return period for selected hierarchical model. (a) Summer, (b) monsoon and (c) annual precipitation.
(a)
(b)
(c)
Results
Longitude
Latitude

## Slide 56
Comparison of return levels for 10 year return period obtained from the selected hierarchical model (Spatial) and from single station (Single) Bayesian analysis for Annual Maximum (AM) precipitation at three stations
Validation

## Slide 58
city
B1
B2
B3
Berlin City boundary
Case study – Berlin City, Germany
Understanding dependence structure of extreme precipitation within an urban area and its surroundings at various durations
Spatial dependence of precipitation analysed with different measures for examining dependence.
Model dependence using max-stable process
Notes: Remove stations in the city
Check the surroundings

## Slide 59
Case study – Berlin City, Germany
Hourly precipitation shows independence within the city even at small distances, whereas the daily precipitation shows dependence.
Both hourly and daily precipitation show dependence as more and more non-urban areas are included.
Geographical covariates are predominant within the city while climatological covariates prevail when non-urban areas are added for the case study.
Notes: Remove stations in the city
Check the surroundings

## Slide 60: Points to remember
Careful assessment of return levels
Propagate parameter uncertainty to obtain projected IDF relationships.
High uncertainty in short duration precipitation extremes.
Uncertainty introduced due to choice of GCM model is smaller than due to parameter uncertainty.
Spatial variation – important to consider
Geographic covariates dominate as drivers of precipitation extremes.
Hourly precipitation shows independence within the city even at small distances, whereas the daily precipitation shows dependence.
Geographical covariates are predominant within the city while climatological covariates prevail when non-urban areas are added for the case study.

## Slide 61: Conclusions
Several uncertainties abound
  With data
  Different models
  Spatio-temporal variability
  Include as much information as possible in modelling
Predictions - consider uncertainty
Assessing flood resilience of a city or system
Better preparedness
Manage flood waters at the source naturally
  Low Impact Development (LID) - storage and reuse
  Sustainable Drainage Systems (SuDS) – permeable pavement, wetlands, green roof, detention basins

## Slide 62: Challenges ahead
Changing climate
Introduces non-stationarity in the process

## Slide 63
https://svs.gsfc.nasa.gov/cgi-bin/details.cgi?aid=3975

## Slide 64: Effect of changes in temperature distribution
IPCC, 2012: Managing the Risks of Extreme Events and Disasters to Advance Climate
Change Adaptation.

## Slide 65: Change in temperature distribution
Distribution of Northern Hemisphere summer temperature anomalies shifting toward an increase in hot summers
https://svs.gsfc.nasa.gov/cgi-bin/details.cgi?aid=3975

## Slide 66: Increase in extreme precipitation
Annual mean extreme precipitation anomaly (mm)
Frequency of events
Source: Papalexiou and Montanari, 2019

## Slide 67: Questions?
Most Welcome!
Contact Information:
chandra.rajulapati@usask.ca
https://twitter.com/ChandraRajulap1