## Slide 1: Learning to Communicate
Robert Calderbank
Duke University
Learn More - IEEE BITS Magazine: A Mathematical Foundation for Communications and Sensing in the Delay-Doppler Domain, Parts I and II – in collaboration with Saif Khan Mohammed, Ronny Hadani, and Ananthanarayanan Chockalingam
Disclosure: Advisor to Cohere Technologies
Abstract: We describe how pulsones interpolate between TDM and FDM, and when it is possible to learn input-output relations without learning the channel, opening the door to machine learning.

## Slide 2: So Many Channels, So Little Time
Doppler
Delay
4G
6G
Today we design wireless systems using mathematical models
This approach is losing ground as wireless channels become more complex and Doppler becomes more significant
Might it be possible to operate model-free
Leo-Satellite Channel
UAV/Aeronautical Channel
mmWave Mobile Channel
Terrestrial Mobile Channel
Terrestrial Pedestrian Channel
Doppler Spread

## Slide 3: We have Asked This Question Before
Newton’s Laws of Motion
Model-based approach that develops understanding
at the most fundamental level.
Kepler’s Laws of Planetary Motion
Model-free approach that uses data to make predictions

## Slide 4: Why Ask It Now?
Machine learning has revolutionized image and natural language processing
Data-driven discovery has revolutionized bioinformatics
*Weinan E, The Dawning of a New Era in Applied Mathematics, Notices of the American Mathematical Society, May 2021
Machine learning (ML) is about approximating functions – broad impact comes from the fact that it is particularly effective in high dimensions
Classically we measure complexity of functions by smoothness – how many times the function can be differentiated
ML measures complexity by how well the function can be approximated by a particular neural network model – reproducing kernel Hilbert spaces, for example

## Slide 5: Localization in Delay and Doppler
Radar as a game of 20 questions with an operator
P.M. Woodward: Probability and Information Theory, with Applications to Radar, Pergamon Press, 1953
He viewed the problem of localizing a scatterer in delay and Doppler as using a waveform to ask questions of the operator defined by the radar scene
How to Design a Question:
Prediction as a game of 20 questions with a doubly spread channel

## Slide 6
|
)
Doppler
shift
Delay
Taps in Delay and Doppler
Representing Doubly Spread Channels
BS
Reflector 1
Reflector 2
Reflector 3
Reflector 4
UE
What is the right question?

## Slide 7: What Constitutes a Good Question?
Time Domain (TD) Pulse: Good question for pure delay channels
Frequency Domain (FD) Pulse: Good question for pure Doppler channels
Doubly Spread Channel: A sum of operators D(ti, nj) introducing path
delay ti and Doppler shift nj
Waveforms are questions, returns are answers, objective is prediction
Delay-Doppler (DD) Domain Pulse: Good question for doubly spread channels

## Slide 8
q
q
q
q
q
q
q
q
q
Quasi-periodicity
A Pulse in the
Delay-Doppler Domain
Fundamental Domain defined by the delay period and the Doppler period
The DD realization of a TD signal is a quasi-periodic function

## Slide 9
TD Pulsone from a Quasi-Periodic DD Domain Pulse
(Delay)
(Doppler)
TD Pulsone
TDM is a limiting case
FDM is a limiting case
Pulsones parametrized by interpolate between TDM and FDM
When does a TD Pulsone question have predictive value?
Notes: 9

## Slide 10
What Constitutes an Ambiguous Answer?
Ambiguity Function|As,s(t, n)|2 We transmit a waveform s to illuminate a radar scene, then correlate the result with the transmitted waveform
TDM: Not able to separate targets in Doppler
FDM: Not able to separate targets in delay
sinc((B - |n|)t)
sinc((T - |t|)n)

## Slide 11
Woodward, 1954
Volume under|As,s(t, n)|2 fixed by Moyal’s Identity but can be redistributed to enable resolution of radar targets
Red Ellipse: Ambiguity function of narrow Gaussian pulse
Modulate a train of narrow TD Gaussian pulses with a broad Gaussian envelope
Black Ellipses

## Slide 12
Pulsones, 2023
Ambiguity Function |As.s(t,n)|2 - pulsone carrier waveform
Narrow DD domain impulses separated by tp along the delay axis and np along the Doppler axis
Each impulse has a spread of 1/B along the delay axis and 1/T along the Doppler axis

## Slide 13
Doubly Spread Channels Acting on Pulsones
Crystalline Regime: The delay domain period tp is greater than the channel path delay spread, and the Doppler domain period np is greater than the path Doppler spread:
tp > delay spread and np > Doppler spread
The interaction of a doubly spread channel with a TD pulsone is predictable and geometric
Twisted convolution:

## Slide 14
Unpredictability results from aliasing in the DD domain
Aliasing occurs when the DD spreads of the channel are bigger than the DD periods of the pulsone
self- interaction leads to unpredictability
Delay spread
Doppler spread
Doppler spread > Doppler period
Delay period
Doppler period
The Origins of Unpredictability

## Slide 15
What is Different in the Crystalline Regime?
No DD Aliasing - the DD spreads of the channel are smaller than the DD periods of the pulsone.
Delay spread
Doppler spread
No Self-Interaction means the channel response is predictable
Doppler spread < Doppler period
Delay spread < Delay period
Delay period
Doppler period

## Slide 16
Twisted convolution:
Picturing Predictability
Wireless channel dynamics lead to replicas

## Slide 17: Crystalline Regime
FDM
TDM
Frequency Selectivity
Time Selectivity
When the fundamental period captures the channel spread the received power profile is flat and the input-output relation is predictable
Doppler spread = 1700Hz
Channel:

## Slide 18
Predictability of the I/O Relation
Relative Prediction Error (RPE) in dB, as a function of delay (horizontal axis) and Doppler (vertical axis) with sinc pulse-shaping filters
RPE minimized at the pulse location
RPE significantly smaller in the crystalline regime

## Slide 19
Delay Doppler
Channel
2
Zak-OTFS baseband Modulation
Channel
Zak-OTFS baseband Demodulation
CHIRRUP
Encoder
[B,K]
K messages (or users) with B bits each
CHIRRUP
Decoder
Block Diagram of Broadcasting
1
1
BS
BS - Base Station
UT - User Terminal
UT1
2
UT2
2
UT3
2
UTK
2
UTK-1
2

## Slide 20: Results (Zak vs MC-OTFS)
BER versus max. Doppler at SNR = 13dB
MER versus max. Doppler at SNR = 13dB

## Slide 21: Non-Fading and Predictable Operation
TDM
FDM
Pulsones in the Crystalline Regime
Delay Spread Only
Doppler Spread Only
Doubly Spread

## Slide 22
Frequency
Time
Delay Doppler
FDM
OTFS
Signal Processing in the DD Domain
Not more complicated than the Fourier Transform
The Fourier Transform as a Composition:
First apply from TD to DD domain, then apply from the DD domain to the FD

## Slide 23: Impact of Fading in the Crystalline Regime
Perfect Channel Estimation: VehA Channel Model
Summary
Performance in the crystalline regime is superior
Performance approaches TDM as the delay period
Performance approaches FDM as the Doppler period

## Slide 24: Predictable means Learnable
Doubly Spread Channels are becoming infinitely complicated
Input-Output Relations can be comparatively simple
Model-Free Operation: It is possible to use pulsones to learn the input-output relation directly without learning the channel

## Slide 25: Model-Free vs Model-Dependent
In the crystalline regime, when it is possible to learn the channel:
Model-Dependent pulsone performance coincides with ideal performance
Model-Free pulsone performance is only slightly inferior

## Slide 26: Model-Free vs Model-Dependent
When it is not possible to learn the channel:
Pulsones support model-free operation in the crystalline regime
Not shown: Improvements in filtering – root raised cosine vs. sinc – extend the region of reliable operation

## Slide 27: Pushing the Envelope – Impact of High Doppler
Model-Free operation in the crystalline regime:
When the Doppler spread 2nmax is bounded away from np then pulsone performance does not degrade as nmax increases
When the Doppler spread 2nmax is close to np then performance degrades because of Doppler domain aliasing

## Slide 28: Navigating Orders of Magnitude in Doppler Spread
Delay Spread
Doppler Spread (KHz)
Leo-Satellite Channel
UAV/Aeronautical Channel (GHz)
mmWave Mobile Channel (28GHz)
Terrestrial Mobile Channel (GHz)
Terrestrial Pedestrian Channel (GHz)
0.8
82
7.0 (Take Off)
33-60 (En-Route)
7.68 (En-Route)
5.0
0.3
1.0
3.0
0.41
0.005

## Slide 29
=
Signal Processing in Zak-OTFS
Zak-OTFS I/O Relation

## Slide 30
=
Signal Processing in MC-OTFS
MC-OTFS I/O Relation

## Slide 31
Zak-OTFS vs MC-OTFS
Predictability of the I/O Relation
Zak-OTFS
MC-OTFS

## Slide 32
Zak-OTFS vs MC-OTFS in the Crystalline Regime
When it is not possible to learn the channel
Performance of model-free Zak-OTFS is superior to that of MC-OTFS because the Zak-OTFS I/O relation is more predictable

## Slide 33
George Orwell: Every generation imagines itself to be more intelligent than the one that went before it, and wiser than the one that comes after it.
1G (1980s)
2G (1990s)
3G (2000s)
4G (2010s)
5G (2020s)
Analog
GSM (pre 3GPP)
IS 95 (pre 3GPP2)
WCDMA (3GPP)
cdma2000 (3GPP2)
LTE (3GPP)
UMB (3GPP2)
WiMax (IEEE)
NR (3GPP)
Voice
Voice / SMS
Data / Voice
Mobile
Broadband
(MBB)
Beyond
MBB
TDMA vs CDMA
CDMA
OFDMA
Scalable OFDM
mmWave

## Slide 34: Reconnecting with CDMA
OTFS
FDM
TDM
CDMA
period curve tpnp=1
in DD domain
Discrete
DD Domain
Continuous
DD Domain
Time Domain
lift
sample

## Slide 35: The Mathematics of Hopping and Spreading
Ntp
Mnp
tp= MDt
np= NDn
Dn
Dt
Dual of the Information Lattice
(kMNDt,lMNDn)
(kMDt,lNDn)
Period Lattice
(kDt,lDn)
Information Lattice

## Slide 36: Conclusions
Doppler
Delay
4G
6G
Bad News: It is becoming impossible to learn channels
Good News: It is still very possible to learn input-output relations
In the crystalline regime: Pulsones enable model-free operation, opening the door to machine learning
What makes this possible? We are using the operators that define doubly spread channels both to probe the channel, and to transmit information

## Slide 37: Pulsones in the Crystalline Regime
Live here, You must
4G/5G
2G
6G
Nonfading, Predictable, Resilient to Doppler